## Slide 1: Christian Valley Park, Community Services District Speed Hump Pros, Cons, & Liability

## Slide 2: Pros
Speeds reduced by ~10 mph
Self-enforcing
Effective long-term speed control without road redesign
Relatively low initial cost
Improved neighborhood safety for pedestrians

## Slide 3: Cons
Potential vehicle damage or injury if crossed at high speed
Large emergency vehicles delayed up to 10 seconds per hump
Higher maintenance
Increased noise from braking, accelerating and compensatory speeding
Potentially reduced property values
May require supplemental lighting to avoid liability

## Slide 4: Steps to Minimize Liability

## Slide 5: Formal Engineering & Traffic Study
An engineering and traffic study documents baseline conditions, which is essential for justification and defense. This includes documenting:
  Traffic volumes
  85th percentile speeds
  Crash/collision history
  Pedestrian/bicycle activity
  Road classification
  Vehicles per day speeding >5 mph over limit

## Slide 6: Verify Design Compliance
Follow Caltrans/CA MUTCD/FHWA standards:
  Parabolic profile: 12 ft long, 3–4 in high
  Spacing: 200–500 ft apart
  Avoid steep grades (>6%), installation near intersections, and drainage issues
Consider alternatives (e.g., speed cushions) if emergency concerns high

## Slide 8: Early Stakeholder Consultation
Mandatory input from emergency services to assess response time impact
Petition residents to demonstrate public need and acceptance (67% resident approval is generally required)
Document all meetings, feedback, and resolutions

## Slide 9: Signage, Markings & Visibility
CA MUTCD-requires:
  Advance warning, which includes W17-1 "SPEED HUMP" sign
  Advisory speed plaque
  Pavement markings: White/yellow reflective striping and chevrons
  Placement near lighting if possible

## Slide 10: Engage Qualified Professionals Document Everything
  Hire licensed engineers, contractors, and inspectors
  Maintain comprehensive records, such as the Engineering & Traffic Survey
  Consultation records, minutes, and emails
  Design drawings and specifications
  Approval resolutions
  Photos of installation
  Maintenance plan

## Slide 11: Post-Installation Monitoring & Maintenance
Conduct before-and-after speed and crash evaluations
Regular inspections
Signage and striping refresh
Asphalt repairs
Prompt response to complaints
Update records annually

## Slide 12: References
California Manual on Uniform Traffic Control Devices (CA MUTCD)
Caltrans Traffic Calming Guide
Placer County Neighborhood Traffic Management Program (NTMP)
FHWA (Federal Highway Administration) Traffic Calming ePrimer
ITE (Institute of Transportation Engineers) Guidelines for the Design and Application of Speed Humps
California Civil Code §1714 (California negligence law)